Parts List:

14-Gauge Wire: Black (4-6 feet)

Yellow (4-6 feet)

Blue (4-6 feet)

White (4-6 feet)

Red (30 feet)

1-bag 4-inch wire tires (As needed)

2-Bosch relays (Part #0332209137)

2-Bosch relay mounts (Part #3334485008)  (To mount the relays inside the door)

4-Eyelet wire attachments (attach wires to a couple of bolts)

20-Non-insulated female receptacles same size as plugs on relay

Heat shrink tubing as needed.

1-“Short Stop” (2-post junction box prevents system from shorting out)

1-bag of insulated male/female connectors (10-14 gauge wire)

Plastic to recover the interior for the door

Cut 6 inches of red wire, attach an eyelet at both ends. Bolt one end to the “short stop” battery end (both poles are noted).  Cut one 10-foot and one 15-foot piece of red wire, connect one end of BOTH wires to an eyelet.  Heat shrink all the eyelet/wire connections.  This will connect to the other pole of the “short stop”.  This will be the power supply to each window relay kit made up of two relays as pictured below.

Bottom Side of Relay Mounts

Relay #1					    Relay #2

Red Wire  (24 inches)

Black Grnd #86

Black Wire 					(24 inches)			      (C         (Connect Relays)														   ##

Red Wire #87

(Connect Relays)			 	B      Blue Wire #30

(18 inches)

White Wire #85

Yellow Wire #30			(18 Inches)

(18 Inches)

White Wire #85

(18 Inches)

These relay mounts will actually slide together to make one unit. The wire colors are noted with the corresponding  plug number on the bottom/plug side of the relay itself.

Either a       or a          notes a junction of wires. If not noted they are the same color.

DISCONNECT THE BATTERY!!!!!!!

Remove the passenger side “A” pillar trim!  You’ll need to loosen the two(2) screws that hold the trim which the passenger sun visor is attached to, and unscrew the trim at the top of the door.  These two(2) screws are hidden beneath the door seal trim at the top of the door frame.  The top of the  “A” pillar will have to be worked out from  underneath these two trim pieces and you’ll need to tap out the three grommets along the length of the “A” pillar.

Once inside the “A” pillar, you will notice a bolt with two large brown wires and one large red wire bolted to it(this is our power source).  This is where you need to connect one end of the 6 inch red wire piece with the two eyelets.  The other end attaches to the “short stopper” (battery end). Don’t tighten it down the bolt all the way because you’ll need to move the wires around.

Feed the shorter of the dual red wires (those that attach to the other end of the “short stopper”) into the body cavity and out via the ground strap (reach in there), then run it along the black wire group into the passenger door (you’ll need to tie-wrap the red wire onto the others later to prevent play or binding).

The longer red wire from the power source needs to be fed into the passenger footwell then across to the driver’s door and into the door like the passenger side.

I used two sided tape to connect the “short stopper” to the “A” pillar, and I put rubber vacuum hose ends onto bolts (two on the “short stopper” and one on the power source bolt)

INSIDE THE DOOR!!!

Remove the door panel by removing the screw at both the front and rear of the door, and CAREFULLY remove the trim pieces around the door handle.  You’ll have to work the door handle out of the trim piece.  There are several wires attached tot the window switch and cigarette lighter.

Cut the wires noted below and attach female/male insulated wire connectors (heat shrink  the end of the connector). I alternated the connectors to avoid improper connections later on.  Leave enough wire so you can mount the relays just behind/above  the door handle.  You’ll need to drill a couple of small (1/8 inch) holes to mount the brackets.

Connect the BLUE relay wire to the GREEN  wire coming out of the window lift motor.

Attach the YELLOW relay wire to the RED wire coming out of the window lift motor.

The WHITE relay  wires connect to the wires that previously attached to the red/green window lift motors. These may need to be reversed so the switch operates in the correct direction.

The BLACK relay wire (with an eyelet at the end) grounds to the bolt on the upper left corner of the door hinge mounting bracket.  There’s probably another ground wire already there, simply use the bolt for both.

The RED wire from the “A” pillar power source needs to be soldered (preferred) or butt connected tot the RED wire of the relay. Make sure you cover any connections with shrink wrap.

Reconnect battery, turn on ignition and try out the window. Tie  wrap everything to tidy up and re-assemble the door.  Do other door.

I’m doing this from pretty vivid memories. Call me at (314) 889-0572 or (314) 249-3770 or (636) 227-2603 if you need help.  Good luck.

Mark Pfeffer